MATERIAL SAFETY DATA SHEET

Company:  WORLD CLASS ATHLETIC SURFACES, INC

817 N. Broad St.

Leland, MS   38756

Phone (662)686-9997		(800)748-9649

SECTION I – PRODUCT INDENTIFICATION

PRODUCT NAME:  World Class Athletic Field Marking Paint – Standard Formula – White, Red, Yellow/Gold, White TMA and Yellow TMA, Green, Old Gold, Blue, Orange

CHEMICAL FAMILY:  MIXED SOLVENTS

LATEST REVISION DATE:  February 2013

SECTION II – HAZARDOUS INGREDIENTS & OTHER COMPONENTS

INGREDIENTS		% Weight 	      EXPOSURE LIMITS  	        CAS #

OSHA PEL      ACGIH TLV

Aliphatic Solvents				      500	        800

V,M&P naphtha				      100			     64742-89-8

Acetone					      750                                             67-64-1

Toluene					108-88-3

Propane                                                                 800	                             68476-86-8

THIS PRODUCT MAY CONTAIN ONE OR MORE MATERIALS SUBJECT TO THE REPORTING REQUIREMENTS OF SECTION 3313 OF THE EMERGENCY PLANNING AND COMMUNITY RIGHT TO KNOW ACTS OF 1968 AND OF 40 CFR 372.  SEE SECTION X FOR SPECIFIC MATERIALS.

SECTION III – PHYSICAL DATA

APPEARANCE / ODOR:  Opaque pigmented liquid with petroleum odor

BOILING POINT:  Concentrate only:  approx 190° F

SPECIFIC GRAVITY (Water=1):  Concentrate only : approx 0.80

VAPOR PRESSURE:  @ 70° F = 35-50 psig

VAPOR DENSITY (Air=1):  > 1	          PERCENT VOLATILE BY WEIGHT: <98%

SOLUBILITY IN WATER:  Insoluble        EVAPORATION RATE (Ethyl Ether=1): <1

SECTION IV – FIRE & EXPLOSION HAZARD DATA

FLAMABILITY CLASSIFICATION:  Extremely flammable aerosol per ASTM

D-3065-77 Flame Extension Test

FLAMMABLE LIMITS:  LEL:  Not Established   UEL:  Not Established

FLASH POINT:  Concentrate only:  Unk

SPECIAL FIRE FIGHTING PROCEDURES:  Keep aerosol containers cooled with water

fog to prevent bursting.

EXTINGUISHING MEDIA:  Foam, CO2, Dry Chemical

UNUSUAL FIRE AND EXPLOSION HAZARDS:  Contents under pressure.  Exposure

of aerosol cans to temperature above 120° F may cause bursting.

SECTION V – HEALTH HAZARD DATA

PRIMARY ROUTE(s) OF ENTRY:   INHALATION:  Yes   DERMAL:  Yes

INGESTION:  Yes

EFFECTS OF OVEREXPOSURE:

SKIN:  Redness, irritation and defatting of skin.

EYES:   Redness, irritation and tearing.

INHALATION:  Respiratory irritation, dizziness, weakness.

INGESTION:  Gastrointestinal irritation, nausea, vomiting, diarrhea.

CARCIOGENICITY:

NTP:  NO	LARC:  NO	OSHA:  NO

MEDICAL CONDITIONS GENERALLY AGGRACATED BY EXPOSURE:  Not

Determined.

EMERGENCY AND FIRST AID PROCEDURES:

SKIN:  Thoroughly with soap and water.  Consult Physician if irritation persists.

EYES:  Flush immediately with water for 15 mins.  Consult Physician if irritation

persists.

INHALATION:  Move to fresh air.  Get medical attention if irritation persists.

INGESTION:  Get immediate medical attention.

SECTION VI – REACTIVITY DATA

STABILITY:  Stable      	CONDITIONS TO AVOID:  Temps above 120° F

HAZARDOUS DECOMPOSITION BY-PRODUCTS:  Carbon Monoxide, Carbon

Dioxide

INCOMPATABILITY:  Strong oxidizers

HAZARDOUS POLYMERIZATION:  Will not occur

SECTION VII – PRECAUTIONS FOR SAFE HANDLING AND USE

STEPS TO BE TAKEN IN CASE MATERIAL IS RELEASED OR SPILLED:  Large

spills are unlikely due to aerosol packaging.  Ventilate area.  Soak up with

absorbent material and dispose of accordingly.

WASTE DISPOSAL METHOD:  When disposing of spent containers, do not puncture

or incinerate.  Dispose of in accordance with local, state, and federal regulations.

SECTION VIII – SPECIAL PROTECTION INFORMATION

RESPIRATORY PROTECTION:  Use NIOSH approved self-contained breathing

apparatus if TLV is exceeded.

VENTILLATION:  Sufficient local or mechanical to maintain vapor concentrations

below TLV.

PROTECTIVE GLOVES:  Solvent resistant.

EYE PROTECTION:  Safety glasses with chemical splash-proof side shields, chemical

goggles and/or face shield.

OTHER PROTECTIVE CLOTHING AND EQUIPMENT:  Sufficient to prevent skin

contact.

SECTION IX – SPECIAL PRECAUTIONS

Keep out of reach of children.  Avoid contact with skin, eyes, or clothing.  Avoid prolonged or repeated exposure to vapors.  Do not store at temperature exceeding 120° F.  Do not use or store around sources of heat, sparks or open flames.  Do not puncture or incinerate.

SECTION X – SUPPLEMENTARY INFORMATION

SARA TITILE III:  RATING SCALE:  0=Minimal; 1=Slight;  2=Moderate; 3=Serious;

4=Severe

HMIS CLASSIFICATION:  HEALTH:  2	FLAMMABILITY:  3  REACTIVITY:  0

NFPA CLASSIFICATION:  HEALTH:  2   REACTIVITY:  0   FIRE:  3

Periodically, users should request new MSDS to assure it matches current formulation.  The above information is accurate to the best of our knowledge.  However, since data, safety standards and government regulations are subject to change and the conditions of handling and use or misuse are beyond our control, no warranty is made either express or implied, with respect to the completeness or continuing accuracy of the information contained herein and disclaims all liability for reliance thereon.  User should satisfy himself that he has all current data relevant to his particular use.